## Slide 1: RISC-V Security Feb 2022

## Slide 2: Intrinsic Security Zero Trust Model
Security as a basic feature of HW, SW Firmware
Support security through entire lifecycle
Guidelines matched to profiles
Root of Trust and Secure Boot
Standards and Certification
Security Ecosystem
Confidential Computing
Isolation
Attestation
Secure Storage
Life Cycle Management
Identity

## Slide 3: Security and RISC-V
RISC-V’s open and clean-slate design presents a unique opportunity to re-think security for the next generation of compute infrastructures.
Become foundation for an Intrinsic Security model
Create robustness against malicious code, bugs, exploits
Enabling Trusted Execution and Confidential Computing – with Zero Trust
Secure App
Secure System SW + Runtimes
Secure Hardware Baseline
Trusted Execution Environment Confidential Computing
Crypto Acceleration
Memory isolation, Control Flow Integrity, Side Channel Protection
Secure App
App
Hardware Root of Trust, Secure Boot
Trusted OS
Rich OS
App
App

## Slide 4: Intrinsic Security RISC-V
Clean Slate architecture – learn the lessons of the past
Security as a basic feature of hardware, firmware, software
Royalty Free – democratising innovation
Embedded
Application
Server
Security Ecosystem
Root-of-Trust, Secure Boot
Side Channel Leakage Protection
Confidential Computing
Trusted Execution Environment
Control Flow Integrity
Memory Protection, Isolation
Crypto Accelleration
Process
Hardware
Security
Capabilities
Firmware,
Software, and
Tools
Processor Cores
Standards Compliance, Security Incidence Response

## Slide 5: RISC-V Security Rationale
Clean-slate architecture invites new hardware security solutions
Open security model accelerates hardware security innovation
Opportunity to incorporate security industry learnings & best practices
Open governance facilitates collaboration on best security approach
Royalty free model enables new open-source hardware security solutions

## Slide 6: Security Organization

## Slide 7: RISC-V Security Scope
Security Model
Security Ecosystem
Memory Safety
Microarchitectural side channels
Robustness
Cryptography
Isolation & TEEs
Confidential Compute
Blockchains
Security Issues & Response (SIRT)

## Slide 8: Security Model
State Goals & Rationale for RISC-V Security
Defines scope
Derives security requirements
Abstracted from implementation specifics
References existing standards when appropriate
Referenced by appropriate sections of Platform specifications
  By Profile, By Vertical

## Slide 9: Security Model
Guiding Principle
Intrinsic security
Zero-Trust
Outline:
Scope, Goals, and Guiding Principles
Security Concerns
Threat Model
Security Topics
Topics:
Lifecycle
Platform Integrity
Data Integrity
Isolation
Secure Boot
Assurance & Attestation
Secure storage
Cryptography
Applicable Standards

## Slide 10: Security Ecosystem
Enablement of RISC-V security services & software
Identify and list key open-source security software and libraries
Develop RISC-V security reference implementation(s)
Identify, monitor, and influence applicable standards
Identify and liaison with applicable Security Certification entities

## Slide 11: Security Ecosystem
Security Services
  Reference implementations
    Secure Boot
    Attestation
    …
  Optimised library ports
    OpenSSL
    mbed Crypto
  OS ports
  APIs, Calling Conventions
Standards and Certification
  Formal Security Proofs
  Certification mapping
Verticals
  Any Specific requirements ?

## Slide 12: Memory Safety
Define strategy for memory protection at the ISA level
Identify improvements that enhance memory security in RISC-V systems
Develop and maintain specifications / ISA extensions for memory safety

## Slide 13: uArchitectural Side Channels
Understand how the microarchitecture is vulnerable to information leakage
Identify potential side-channel and covert-channel information leakage
Develop strategy to prevent microarchitectural information leakage in RISC-V systems
Develop and maintain specification/recommendations that mitigate microarchitectural side channels

## Slide 14: Leakage Protection
Speculation Barriers
  ISA extensions to control uArch ?
    Fence.t

## Slide 15: Robustness
Understand how malicious actors manipulate and exploit (unexpected) system behavior
Identify capabilities that improve system level robustness under adversarial conditions
Define strategy that will improve robustness of RISC-V systems at ISA or non-ISA level
Develop, maintain, or support creation of specifications as needed

## Slide 16: Robustness
Control Flow Integrity
  BTI, Shadow Stack, PAC etc
Capability Based
  CHERI JWG
  Alternatives ?

## Slide 17: Cryptography
Understand the landscape of cryptographic schemes and threats against established cryptography
Identify what cryptographic primitives, constructs, and algorithms are in-scope for RISC-V
Develop and maintain crypto related specifications

## Slide 18: Isolation & TEEs
Identify what technologies enable isolation and Trusted Execution Environments (TEEs)
Define how isolation/TEEs can be implemented on RISC-V systems
Create gap analysis to identify missing components
Develop, maintain, or support creation of specifications for Isolation/TEEs

## Slide 19: Trusted Execution
Memory Safety
  PMP based TEEs
Hardware based Isolation
  M-Class secure functions
  A-Class Maintaining privilege levels in TEE
  System Awareness
Attestation of entire software chain from initial boot
Attestation of applications/workloads isolated by TEE
Security aware Debugging and performance monitoring
Maybe ISA affecting / ISA Affecting

## Slide 20: AP-TEE & Confidential Compute
Survey Confidential Compute and AP-TEE technologies
Define requirements that enable Confidential Compute on RISC-V systems
Create technology gap analysis for RISC-V
Develop, maintain, or support creation of specifications as needed

## Slide 21: Confidential Compute
Mutually untrusted applications
Isolated Application Enclaves
Encrypted Enclaves
VM Enclaves
Incorporate attestation standards from e.g., Confidential Computing Consortium, DMTF, and TCG
Leverage AP-TEE where applicable
Maybe ISA affecting / ISA Affecting

## Slide 22: Blockchains
Define requirements for enabling blockchains/distributed ledgers on RISC-V systems
Identify and address RISC-V technology gaps in enabling distributed ledger technologies
Create use cases and developer guidelines for deploying blockchains/distributed ledgers on RISC-V systems

## Slide 23: SIRT
Ensure continuity of the RISC-V Security Incident Response Team (SIRT)
Institute and manage a responsible disclosure process
Triage incoming security disclosures
Maintain a catalogue of security issues

## Slide 24: Gap Analysis

## Slide 25: Competition (Work-in-Progress)
Feature |  | arm | intel | AMD
Comprehensive Ecosystem | SBI definition, OPEN SBI, Keystone TEE Framework | Standard Security APIs Open Firmware Reference Implementations Security Model | Standard Security APIs Reference Implementations | Standard Security APIs Reference Implementations
Trusted Execution Environment | PMP based TEE, Hypervisor support, S-Mode MPU (no isolation at m-mode) | Trustzone A/M class HW TEE | Intel TXT, Intel VT-x | AMD SVM
Confidential Compute |  | v9A Realms - Confidential Compute Architecture | Intel TDX – Confidential VM Architecture Intel SGX – Confidential Applications Architecture | AMD SEV (-ES, -SNP) - Confidential VM Arch.
Arbitrary Privileged Code Execution | ePMP, NX/SMAP/SMEP | Privilege Access Never | NX/SMAP/SMEP | XD/SMAP/SMEP
Control Flow Integrity |  | Branch Target Identifier Pointer Authentication Code | Indirect Branch Tracking Shadow Stack | Shadow Stack
Memory Safety | ePMP | Memory Tagging Extension |  | 
Side Channel Leakage |  | Speculation Barriers | Speculation Barriers | Speculation Barriers
Cryptography | AES, SHA2, SM3, SM4, entropy, Data Independent Execution Latency | AES, SHA2, SHA3, SM3, SM4, RNG, Vector | AES, SHA, RNG, AVX-512 | AES, SHA, RNG, AVX2
Crypto library |  | AArch64cryptolib | Intel IPP Cryptography | AMD Optimizing CPU Libraries

## Slide 26: Competition (Work-in-Progress)
Feature |  | arm | intel | AMD
Comprehensive Ecosystem | SBI definition, OPEN SBI Keystone TEE Framework | Standard Security APIs Open Firmware Reference Implementations Security Model | Standard Security APIs Reference Implementations | Standard Security APIs Reference Implementations
Trusted Execution Environment | PMP based TEE, Hypervisor support, S-Mode MPU (no isolation at m-mode) | Trustzone A/M class HW TEE | Intel TXT, Intel VT-x | AMD SVM
Confidential Compute |  | v9A Realms - Confidential Compute Architecture | Intel TDX – Confidential VM Architecture Intel SGX – Confidential Applications Architecture | AMD SEV (-ES, -SNP) - Confidential VM Arch.
Arbitrary Privileged Code Execution | ePMP, NX/SMAP/SMEP | Privilege Access Never | NX/SMAP/SMEP | XD/SMAP/SMEP
Control Flow Integrity |  | Branch Target Identifier Pointer Authentication Code | Indirect Branch Tracking Shadow Stack | Shadow Stack
Memory Safety | ePMP | Memory Tagging Extension |  | 
Microarch. Side Channels |  | Speculation Barriers | Speculation Barriers | Speculation Barriers
Cryptography | AES, SHA2, SM3, SM4, entropy, Data Independent Execution Latency | AES, SHA2, SHA3, SM3, SM4, RNG, Vector | AES, SHA, RNG, AVX-512 | AES, SHA, RNG, AVX2
Crypto library |  | AArch64cryptolib | Intel IPP Cryptography | AMD Optimizing CPU Libraries
Trusted Computing SIG
Memory Safety SIG
CFI SIG
Memory Safety SIG
uArch Side Channel SIG
Crypto TG

## Slide 27: Status & Roadmap

## Slide 28: 2021 Highlights
New Chair and Vice-Chair (mid-year)
enhanced-PMP specification ratified
Crypto Scalar specification ratified
SIRT process defined
Draft S-mode MPU specification
New SIGs: Blockchain, CFI, and uArchitectural Side Channel
Refocused & renamed Security Tech SIG to Trusted Computing SIG
IOMMU effort launched under Software HC

## Slide 29: Roadmap (Work-in-Progress)
2022
2023
Security Model
Lightweight TEE
AP-TEE TG + Cap-based TG (?)
S-mode MPU
International Scalar Crypto
Microarchitectural Side Channel (uSC) leakage mitigations
Ecosystem, Reference implementations, etc.
2021
Scalar Crypto
ePMP
IOPMP
Vector Crypto
PQC Crypto
IOMMU within Software HC
uSC TG(s): Temporal Fencing and others (?)
Control Flow Integrity (CFI)
SIG work
CFI TG(s)
Blockchain whitepaper
TG work
HC work
Application-TEE, Confidential Compute, and Capabilities-Based (AP-TEE)
IOMMU
Pointer Masking (J extension)
Memory Tagging

## Slide 30: Long-Term Priorities
Security Incident Response Team (SIRT) maintenance
Platform Security Model creation
Platform Security Model and RVI Platforms integration
Security functionality competitive / gap analysis
Enhanced cryptography functionality
Microarchitectural side channel leakage mitigations and Control Flow Integrity capabilities
Enhanced memory security model
Define RISC-V architecture for TEEs and Confidential Computing
Security (software) ecosystem enablement
Capability-based solution(s)

## Slide 31: 1st Half 2022 Targets
Competitive gap analysis & Roadmap
SIRT process integration & communication
Draft Platform Security Model
Blockchain SIG (draft) white paper
Control Flow Integrity SIG strategy recommendations
Trusted Computing SIG architecture recommendations
Microarchitectural Side Channel SIG strategy recommendations
Memory Safety SIG creation
Crypto Vector draft specification
International Crypto TG

## Slide 32: RISC-V Security 5 year horizon
Platform Security Model outlining RISC-V security capacities and system’s integration
Tools and Software support for RISC-V security capabilities
Protection against side-channel information leakage at the hardware level
Robustness capabilities to prevent malicious manipulation of e.g., code execution flows
Cryptography support for small to large devices, including Post-Quantum Crypto
Memory isolation and Trusted Execution Environments to securely separate applications from each other
Support for Confidential Compute models to enhance application and data privacy
Blockchain technology on RISC-V based systems

## Slide 33: Backup